## Slide 1
Sparse Transform and Compressed Sensing for MRI Image Reconstruction
Group 16:
P. Sathvik - 24240
Ch. Uday - 24210
G. Varshini - 24216
K. Sai Ganesh - 24226

## Slide 2
What is MRI?
MRI (Magnetic Resonance Imaging) is a medical imaging technique
Used to see brain, spine, organs, tissues
Produces high-quality images
Problem: MRI scan takes 30–40 minutes
Long scan time causes:
  Patient discomfort
  High hospital cost
  Large data storage

## Slide 3
Problem Statement
MRI collects a huge amount of data
Full data collection = long scan time
If we reduce data → image quality decreases
Goal:
  Get good-quality MRI images using less data and less time

## Slide 4
What is Compressed Sensing (CS)?
Compressed Sensing is a smart signal processing technique that:
Uses fewer measurements
Still reconstructs the original image accurately
“We don’t need all data if the image is sparse.”

## Slide 5
Key Principles of Compressed Sensing
Sparsity
  Image has many unimportant values
  Only few important coefficients matter
Incoherent Sampling
  Randomly collect data (not line by line)
  Avoids repeating similar information
Non-linear Reconstruction
  Use optimization algorithms
  Recover image from incomplete data

## Slide 6
Why Compressed Sensing is Important for MRI
Reduces MRI scan time
Less patient discomfort
Faster diagnosis
Lower storage and computation cost
Maintains diagnostic image quality

## Slide 7
To simulate under sampled MRI reconstruction.
To implement sparse transform-based reconstruction
algorithms.
To compare reconstruction quality using different methods.
To analyze trade-offs between image quality and computational complexity.
OBJECTIVES

## Slide 8
Input MRI image acquisition
Image preprocessing and normalization
Transformation to sparse domain
Random under-sampling of coefficients
Inverse reconstruction
Performance evaluation using image quality metrics
METHODOLOGY

## Slide 9
The paper compares 4 algorithms:
DWT - Discrete Wavelet Transform
FFT - Fast Fourier Transform
DCT - Discrete Cosine Transform
Basis Pursuit (BP) - True Compressed Sensing method
Reconstruction Methods Used

## Slide 10
You take a big picture (MRI scan).
You break it into smaller building blocks (wavelet coefficients).
You keep only a random portion of those blocks (sampling).
You try to rebuild the picture from those fewer blocks.
Finally, you check how close the rebuilt picture is to the original.
Pros: Preserves edges
Cons:
  Not consistent with real MRI physics
  Image quality is low
Algo 1:- DWT – Discrete Wavelet Transform

## Slide 11
Algo 1:- DWT – Discrete Wavelet Transform
LL (Approximation) - Overall shape and smooth regions
LH (Horizontal Details) - Horizontal edges
HL (Vertical Details) - Vertical edges
HH (Diagonal Details) - Fine textures and noise
LL- Low pass filter applied to rows and columns
LH – Low pass filter to rows , high pass filter to columns
HL – High pass filter to rows , low pass filter to columns
HH - High pass filter applied to rows and columns

## Slide 12
You take a big picture (MRI scan).
You convert it into frequency components.
You keep only a random portion of those frequency components (sampling).
You try to rebuild the picture using the inverse FFT from those fewer components.
Finally, you check how close the rebuilt picture is to the original.
Pros: Physically related to MRI
Cons: Visible noise and artifacts
Algo 2:- FFT – Fast Fourier Transform

## Slide 13
Algo 2:- FFT – Fast Fourier Transform
Fast Fourier Transform (FFT) decomposes an image into its frequency components.
Instead of sub-bands like DWT, FFT represents the image using low and high frequencies.
Each frequency component indicates how rapidly pixel values change.
Low-Frequency Components (Center – low freq information)
  Represent smooth regions and overall illumination
  Contain most of the image energy
High-Frequency Components (Outer Regions – high freq information)
  Represent edges, sharp transitions, and fine details
  Capture textures and noise
  Found away from the center of the spectrum

## Slide 14
Results
Sampling rate 0.35

## Slide 15
Results
Sampling rate 0.5

## Slide 16
Results
Sampling rate 0.7

## Slide 17
Results

## Slide 18
Comparative Analysis: DWT vs FFT
Feature | DWT (Algorithm 1) | FFT (Algorithm 2)
Domain | Wavelet (time–frequency) domain | Frequency (k-space) domain
MRI Relevance | Not physically consistent with MRI | Physically consistent with MRI acquisition
Visual Quality | Grainy, patchy reconstruction | Clearer image with better structure
RMSE( Root Mean Square Error) | Higher (more error) | Lower (less error)
PSNR(Peak Signal to Noise Ratio): | Lower image quality | Higher image quality
SSIM(Structural Similarity Index) | Moderate structural similarity | Better structural similarity
Computation | Fast and simple | Fast and efficient
Overall Performance | Moderate | Better than DWT

## Slide 19
Thank You